## Slide 1
Dual-Track Inductive Encoder based on MCXA34x
Key Advantages
• Ultra-thin hollow-shaft PCB form factor
• 16/15 Vernier dual-track absolute angle
• High immunity to magnetic field interference
Core Features
• Dual AS5715R paths for 16-cycle and 15-cycle tracks
• 4-channel synchronous LPADC sampling
• Offset, gain, phase and ellipse correction
• atan2 phase extraction and Vernier branch solve
• Type-II software PLL with velocity output
• Flash calibration with CRC and fallback defaults
• T-Format, BiSS-C and FreeMASTER support
Target Applications
• Robotic joint modules
• Heavy-load gimbals
• Servo motors
• Automotive actuators (EMB, SBW)
Dual RX coil PCB / rotor
Track A1
16-cycle sin/cos
AS5715R #1
Track A2
15-cycle sin/cos
AS5715R #2
RC filter / OPA / TLV9062
MCXA344
sync LPADC0/1
atan2 + 16/15 Vernier
Type-II PLL
T-Format / BiSS-C / FreeMASTER
Motor Driver / PLC / Host
↓
↓
↓
↓
↓
↓
Compact hollow-shaft hardware with 16/15 Vernier absolute-angle output

## Slide 2
Second-Generation Dual-Track Encoder Principle
Upgrade Concept
Ø Two sensing tracks on one rotor-stator set
Ø 16-cycle track provides fine electrical phase
Ø 15-cycle track resolves the absolute branch
Vernier Angle Synthesis
Ø phi16 - phi15 changes once across a full turn
Ø phi16 refines the sub-cycle position
Ø Absolute 0-360° angle without magnet or gear
System Benefit
Ø 16-bit single-turn output for servo-class feedback
Ø Branch-slip guard improves single-frame glitch immunity
Ø Multi-turn accumulation remains firmware-managed
Dual RX coil PCB
16-cycle + 15-cycle
tracks
Rotor target
single mechanical
turn
↔
Second-generation sensing principle
Track A1
16 electrical cycles
sin16 / cos16
Track A2
15 electrical cycles
sin15 / cos15
↓
↓
MCXA344 analog front end
OPA / TLV9062 + synchronized LPADC
↓
Vernier absolute-angle solve
coarse = wrap(phi16 - phi15)
angle = coarse + (phi16 - 16·coarse) / 16
↓
16-bit single-turn absolute angle
plus RAM multi-turn accumulation
Two electrical tracks resolve both fine phase and absolute branch in one turn

## Slide 3
Second-Generation Decoding Flow
Signal Path
Ø Four ADC channels capture A1/A2 sin/cos pairs
Ø Offset, gain and phase errors are calibrated
Ø atan2 converts normalized vectors to track phase
Stability Layer
Ø Type-II software PLL publishes a low-noise angle
Ø Velocity estimate is generated inside the tracker
Ø Output hysteresis suppresses static display jitter
Production Readiness
Ø Flash calibration storage with CRC and fallback defaults
Ø Runtime trim compensates amplitude drift over a revolution
Ø Status bits report weak tracks, ADC rail and mismatch
4-channel LPADC
A1/A2 sine and cosine sampled synchronously
↓
Ellipse correction
center removal + T matrix normalization
↓
atan2 phase extraction
phi16 and phi15 per sample
↓
16/15 Vernier solver
branch selection + fine-angle refinement
↓
Type-II tracking observer
stable angle and velocity output
↓
Published results
angle_counts, multi_turn_deg, status
Factory
calibration
center, ellipse,
zero
Runtime trim
mag window +
AGC
Diagnostics
weak / rail /
mismatch
Calibration, Vernier solving and tracking convert raw signals into stable results